# ISO Thread Specifications
Metric threads only.
M 16 x 2 - 4h -5H
- M --- ISO Metric designation
- 16 --- Nominal diameter in millimeters
- 2 --- Thread pitch in millimeters (distance from top of one thread to top of the next)
- 4h --- Class of fit of this thread (optional)
- 5H --- Class of fit of mating thread (optional)